Datasheet A461

Pneumatic sealer

Pneumatic sealer

Characteristics

| Strapping qualities: | Uniflex and Ultraflex max. 1100 N/mm2 / 160’000 psi |
| --- | --- |
| Strapping dimensions: widths | 19.0 – 32.0 mm / 3/4 – 1 1/4” |
| thicknesses | 0.63 – 1.00 mm / .025 - .040” |
| Weight: | 4.2 kg / 9.3 lbs |
| Average seal strength: | Approx. 75 % |
| Seals: | Overlap seals |
| Type of joint: | Double notch upcut joint |
| Tensioning: | With separate tensioner model A452 |
| Two different working versions: | Version N = Handle 90°to the strap (normal) |
|  | Version P = Handle parallel to the strap |

Advantages

The pneumatic sealer can be used easily with one hand only

The safe upcut double notch joint is accomplished in one strike

The seal safety mechanism prevents poor seal joints as a result of faulty operation of the tool by the user

The tool can be supplied with the handle in a 90° angle to the strap (N-version) or with the handle parallel to the strap (P-version), the user may select the right tool for his application

| FROMM Holding AG | Tel. +41 (041) 741 57 41 |
| --- | --- |
| Hinterbergstrasse 26 | Fax +41 (041) 741 57 60 |
| CH-6330 Cham | www.fromm-pack.com |
| Switzerland | hold.ch@fromm-pack.com |

Datasheet A461

Pneumatic sealer

Chart of types model A461 – Version N = Handle 90°to the strap

| Item No. | Model | Width | Uniflex | Ultraflex |
| --- | --- | --- | --- | --- |
|  |  |  |  | Thicknesses | Thicknesses |
|  |  | mm | inch | mm | inch | mm | inch |
| 13.4310 | A461/19/0.63-0.70/N | 19 | ¾“ | 0.63-0.70 | .025-.028 | 0.63-0.70 | .025-.028 |
| 13.4312 | A461/19/0.80-1.00/N | 19 | ¾“ | 0.80-1.00 | .030-.040 | 0.80-1.00 | .030-.040 |
| 13.4410 | A461/25/0.80-1.00UNI/0.80-0.90ULT/N | 25 | 1“ | 0.80-1.00 | .030-.040 | 0.80-0.90 | .030-.035 |
| 13.4510 | A461/32/0.80-0.90/N | 32 | 1 ¼“ | 0.80-0.90 | .031-.035 | 0.80-0.90 | .030-.035 |
| 13.4512 | A461/32/1.00UNI/N | 32 | 1 ¼“ | 1.00 | .040 | - | - |
| Uniflex | = Regular duty strapping max. 850 N/mm2 / 123'000 psi |  |  |  |  |
| Ultraflex | = High tensile strapping max. 1100 N/mm2 / 160'000 psi |  |  |  |  |

Chart of types model A461 – Version P = Handle parallel to the strap

| Item No. | Model | Width | Uniflex | Ultraflex |
| --- | --- | --- | --- | --- |
|  |  |  |  | Thicknesses | Thicknesses |
|  |  | mm | inch | mm | inch | mm | inch |
| 13.4311 | A461/19/0.63-0.70/P | 19 | ¾“ | 0.63-0.70 | .025-.028 | 0.63-0.70 | .025-.028 |
| 13.4313 | A461/19/0.80-1.00/P | 19 | ¾“ | 0.80-1.00 | .030-.040 | 0.80-1.00 | .030-.040 |
| 13.4411 | A461/25/0.80-1.00UNI/0.80-0.90ULT/P | 25 | 1“ | 0.80-1.00 | .030-.040 | 0.80-0.90 | .030-.035 |
| 13.4511 | A461/32/0.80-0.90/P | 32 | 1 ¼“ | 0.80-0.90 | .031-.035 | 0.80-0.90 | .030-.035 |
| 13.4513 | A461/32/1.00UNI/P | 32 | 1 ¼“ | 1.00 | .040 | - | - |
| Uniflex | = Regular duty strapping max. 850 N/mm2 / 123'000 psi |  |  |  |  |
| Ultraflex | = High tensile strapping max. 1100 N/mm2 / 160'000 psi |  |  |  |  |

| FROMM Holding AG | Tel. +41 (041) 741 57 41 |
| --- | --- |
| Hinterbergstrasse 26 | Fax +41 (041) 741 57 60 |
| CH-6330 Cham | www.fromm-pack.com |
| Switzerland | hold.ch@fromm-pack.com |